## Slide 1: SECURE HOME GATEWAY PROJECT
CIRA Labs
Secure Home Gateway
Project Update
Jacques Latour
March 2019
Notes: Consider starting with a story of your vision – how did this come to be?

## Slide 2: Project Evolution – From Idea in late 2016
Need security access controls
Need a new framework to prevent lightbulbs from killing the internet!
Has to be easy to use
In the home
Gateway
x
x
?
MIRAI Dyn Attack
October 2016

## Slide 3: The many problems of today’s Home Gateway
No Standard Home Network Security Framework
No standard onboarding process
No outbound traffic security controls
Not globally reachable (no domain name)
No unique WIFI keys per home device
No device quarantining processes
No visibility on network activities
Home
Gateway

## Slide 4: IoT Device Security Landscape
Many are Vulnerable
Software is out of date
Time to market -
Not to build correctly
Contribute to DDoS attacks
Cloud architecture dependencies
Compromise your network
Steal private information
Record video and voice
Steal WIFI credentials
Distribute malware
Send spam
Some are Unsupported
Many standards being developed
Full access to the ENTIRE Internet
Lack of secure testing and design
Require active monitoring

## Slide 5: IoT vendors are creating dependency on cloud architecture
At home
IoT Cloud
Services
On the road
Direct is better
Personal information is of great value to vendors
IPv6 with CIRA delegated names for the home makes this possible

## Slide 6: We put a team together to work on the idea
CIRA Labs
Sandelman Software
TwelveDot
Viagénie
TELUS
/ Algonquin College
SIDN Labs
Canadian Multistakeholder
Process: Enhancing IoT security
iotsecurity2018.ca
Secure Home Gateway
Project

## Slide 7: Project Evolution – To a Secure Home Gateway (SHG) Prototype
MUD Server Repository / Curation
Secure
Home
Gateway
openWRT
Turris Omnia
CZNIC
SHG MUD Controller
Supervisor
SHG App “Ease of Use”
SIDN (.NL) SPIN
prpl Foundation
(prplWrt)
Mozilla IoT -
Web Thing API
SHG Security Access Controls
CIRA
DNS & SHG Provisioning
Standards Development
IETF, CSA/UL, ISO/IEC
Enhanced WIFI security
In progress:
DOTS, DNSSEC, Domain aware NFtable
Secure Home Gateway Framework
Running
Code
Proposed
Standards

## Slide 8: Let’s look at the solution we have so far

## Slide 9: Secure Home Gateway (SHG) Goals
x
x
Protect the internet from IoT devices attacks
Protect IoT devices from the internet attacks
Notes: The primary goal of this project is to develop a secure home gateway that;
  protects the internet from IoT devices attacks and
  protects home IoT devices from the internet attacks

## Slide 10: Current state of Home Gateways
Users don’t know who to contact when there is a security issue either with their devices or network.
Devices and current home gateways are not secure by default
Users typically lack the technical know-how to configure the devices. These technologies and their configurations are typically technically complex which results in many using default configurations or users making mistakes when configuring them.

## Slide 11: Scope of work
Develop functional prototype
Open source code
Simple management interface
Framework to provision SHG
domain names
New standards requirements
Enhance small network privacy & security
Notes: We are developing an advanced security framework for small network (home and small business) gateways based on integrating existing and emerging technologies & standards
Goals:
  Develop a functional SHG prototype
  Develop a simple management interface to provision complex network
  Identify new standards requirements and updates
  To enhance small network privacy & security with ‘intent based’ network access controls
  To have open source running code & standards
  Develop a framework to provision SHG domain names

## Slide 12: Best practices – Apply enterprise security framework to home networks
Home Security
PDAP
Appliances
PDAP
Sensors
PDAP
Management
Application
IoT Cloud
Services
PDAP: Per Device Access Policy
Scale Enterprise solutions to fit the home network
Notes: -> best practices and new standards (note to Jacques – please explain Per Device Access Policy (PDAP) for those who may not understand what it means)
Rule #1: Identify IoT devices on your home network
Rule #2: Place a policy around the IoT device that restricts it to a specific function (default is no access)
Rule #3: Monitor for behavioural changes in the device and quarantine at the first sign of change.

## Slide 13: New standards – MUD - Manufacturer Usage Description – RFC8520
I’m an ACME water sensor
- MUD File at: https://acme.corp/mud/ws1.0.json
MUD FILE:
- I have WIFI & apply the water sensor access policy
- I need to upgrade my firmware at https://acme.corp
- Configure me at https://myip/setup
- Alerts available at https://myip/alerts
It would be nice if the IoT device could advertise it’s current firmware version and/or current MUD file URL via WIFI or network connection (DPP, DHCP, LLDP…) on order to setup correct security profile

## Slide 14
MUD Controller
(1)
Scan MUD
QR code &
send to MUD
Controller
(DHCP in future)
CIRA SHG
MUD Repository
SHG
App
(2)
Send to
CIRA
(2)
Get vendor
MUD file
ACME.CORP
MUD
Repository
SHG
ACME.CORP
IoT Water Sensor
(1)
(3)
User accepts
provisioning
instructions
MUD QR Code
(1)
(4)
IoT device added to network with specific network access controls
Network Access control:
Allow access to ACME.CORP
Allow to send alerts internally
Allow to be configured by app
Deny all other internet access
(4)
(IP Tables)
MUD Supervisor
Notes: High Level MUD & IoT Device Provisioning Workflow

## Slide 15: Work in progress architecture

## Slide 16: That’s why we need a simple provisioning interface – this stuff is complex!!

## Slide 17: Removing end-user complexity
A simple user interface
Notes: Simple user interface
The previous slides have outlined the high level workflow. The actual workflow and automation can be very complex.
One key goal of this project is to present the users with very simple choices to provision and administer a potential complex network.
Ideally, the user can only swipe up, down, left and right.

## Slide 18: Quarantine of compromised devices -> Behavioural analysis
A standard process to quarantine and restore IoT Devices
https://datatracker.ietf.org/doc/draft-richardson-shg-un-quarantine
Manufacturer Usuage Description for quarantined access to firmware
https://datatracker.ietf.org/doc/draft-richardson-shg-mud-quarantined-access/
Appliances
Management
Application
x
The refrigerator is quarantined
- Bad lettuce 

## Slide 19: Secure remote access: Trusted authentication & accessible
Mobile
n3CE618.router.securehomegateway.ca
The prototype will use securehomegateway.ca 3rd level domains
22
Notes: Removing the complication surrounding enabling trusted secure remote access to home network is a key goal of this project (not for the initial prototype)
Need an internet resolvable domain name for the SHG to remotely connect. i.e. “myhome.ca”

## Slide 20: Automation
+
Secure gateway
provisioning automation
Secure device
provisioning automation
INNOVATION
Notes: The focus is on automation

## Slide 21: Step 1 – bundle with a DNSSEC signed 3rd or 4th level .CA domain
+
QR Code to activate provisioning and domain
3rd level domain
domain.securehomegateway.ca
4th level domain
domain.router.securehomegateway.ca
+
Notes: When you buy a CIRA secure home gateway, it comes bundled with a DNSSEC signed 3rd level .CA domain.

## Slide 22: Step 2 – Secure Home Gateway setup
SHG
application
https://datatracker.ietf.org/doc/draft-richardson-anima-smarkaklink/
BRSKI enrollment of with disconnected Registrars – smarkaklink
This document details the mechanism used for initial enrollment using a smartphone of a BRSKI Registrar system.
…where the registrar device is new out of the box and is the intended gateway to the Internet (such as a home gateway),
but has not yet been configured…
kaklink 
Notes: Follow the configuration instructions
  Install & open the CIRA SHG App
  Power on the SHG
  Scan the SHG QR code for initial setup
  System Assigned 3rd level domain name
  Setup split view Internet/External DNS for SHG domain
  Home Gateway ready for configuration

## Slide 23: Step 3 – External DNS/DNSSEC Provisioning
SHG External
Domain Provisioning
& Primary DNS
External
DNS view
Hidden Primary
Internal
DNS view
Secondary DNS
D-Zone
SHG External
IP Address
Notes: Automated DNS Backend Provisioning @ CIRA
  CIRA creates the 3rd level .CA SHG domain w/DNSSEC
  SHG and CIRA sync on external view propagation, internal SHG DS record synced in external DNS view. (full chain of trust internally and external on SHG domain)
  Need synchronisation between external SHG DNS record and SHG external IP address

## Slide 24: Step 4 – Automated Wi-Fi setup
Scan
MUD profile
Wi-Fi credentials
Device access policy
Notes: Current focus is on automated Wi-Fi setup – that’s challenging!
Setup secure home network infrastructure
  Using your SHG App, scan the QR code of each new device to:
    Discover the MUD profile
    Transfer the unique WIFI credentials (per MAC address)
    Assign the appropriate Device Access Policy

## Slide 25: Simple user interface is key to this project
Swipe UP, DOWN, LEFT and RIGHT
Notes: Gateway provisioning, device discovery, device provisioning must be as simple as possible, intuitive for non experienced users, available as framework for default open source app.

## Slide 26: Roadmap: Future functionality
Notes: Next slides include things we identified for potential future work or functionality
Includes ideas, comments & feedback

## Slide 27: IoT service / action type – Generic IoT home controller
Notes: Status: Up/down, on/off, ok/bad, status variable
Audio/Video: Camera, video feed
Media: Audio/Video media feed, TV, music
Storage: Data storage, NAS (pictures, files, data)
Alerts: Up/down, on/off, ok/bad, “Water detected”
Control: Turn up/down, on/off, change device value
Cloud Service: IoT vendor, Google, MS, DropBox
VPN (VPN inside vpn.myhouse.ca)
Remote house access
Quarantine, New MUD profile available
Other Sensors/ Actuator functions?

## Slide 28
Adding remote VPN access to trusted mobile and computers
Mobile
(1) Discovery services
(2) Grant permission and credentials to mobile for remote home access
28
31

## Slide 29: Should the inside of your car be part of your home network as well?
29

## Slide 30
Adding your car
30
Car
(1) Discovery services
Control car feature
View car alerts
View car status/location
(2) Assign roles
32
Notes: Adding your Car to remotely access your home network

## Slide 31: There are many more IoT scenarios to be assessed!
Notes: List of IoT scenarios to be assessed
Example of pushing WIFI to the device
Show that the fridge is exposing service
No web interface on IoT device
Focus on cloud / vendor, show they integrate into this solution, can be multi vendor multi cloud provides
IoT Classification: based on device type, air play could see all camera in the house, the TV could see all camera (security controls)
Door bell sends to audio device, you car
Fire alert send to audio receiving device
SmartGRID company allow access to home gateway
  allow SmartGRID to access hot water tank
  allow SmartGRID to adjust thermostats

## Slide 32
This slide deck is a vision
it’s what we’ll be seeing in five years.
Notes: Is work in progress, presented as a story
  Story how a home gateway can be user and IoT friendly
Is meant to define a security framework and associated standards
  IETF, ISO/IEC, others..
Is tuned around implementation at .CA / CIRA, but not specific just for CIRA
Is to solicit feedback
Is another layer of defence (in depth) to protect the internet against nasty (IoT) devices

## Slide 33: Want more info?
Visit the CIRA Labs page and as well as GitHub
https://cira.ca/cira-secure-home-gateway
https://github.com/CIRALabs
Don’t forget to share your feedback and input!
Notes: For an informational version of this deck that includes:
High level architecture graphic
More details on the proof of concept and prototype
Specifications we are currently leveraging

## Slide 34
Questions?

## Slide 35
Our assessment of the home network and IoT security posture post MIRAI attack clearly identified a need for additional home security measures to protect the internet from compromised IoT devices and a very strong need for an enhanced open source home security framework.
Our work so far has identified a significant gaps in open source projects to implement an enhanced home security framework
We embarked on a journey to identify these gaps and start development of many open source projects to better the internet 

## Slide 36: Why are we working on this? -> Risk mitigation
For many internet organizations like CIRA the #1 risk on the risk register is a large scale (Dyn like) DDoS attack.
One of the mitigation mechanisms for this risk is to prevent ‘weaponization’ of IoT devices
Tightly controlling access ‘to’ and ‘from’ IoT devices inside the home or small office network is key to preventing ‘weaponization’ and causing harm on the internet.
The threat that IoT devices bring is the scale of attacks. The uncontrolled access of million/billions of IoT devices to and from the internet is the threat we need to mitigate.

## Slide 37: Overview of the IoT threat landscape -> Scale and capacity
IoT device compromises:
  Used in internet attacks i.e. MIRAI/DYN Attack (DDoS) targeting DNS servers (~1.2 Tbs)
IoT traffic generation, reflection and amplification
  IoT device used various attacks (DDoS) NTP, DNS, SNMP and new vectors.
  IoT device have the capacity to generate large traffic load
  Home and small office network now starting to have gigabit internet access speed, significantly impacting the capacity to create powerful attacks

## Slide 38: High Level Architecture (very ;-)
OpenWrt
Home Gateway
Home Network
CIRA SHG Registry
Internal DNS/DNSSEC
External IPSEC
D-Zone firewall
3rdlevel.securehomegateway.ca
Home Gateway
Provisioning
3rd Level .CA home domain
Primary DNS
D-Zone
IoT Cloud
Services
&
D-Zone Firewall
Secure Remote Home Network Access
Wifi MiFi Zigbee
NFC RFID

## Slide 39: We are building a Prototype -> Based on Omnia Turris Gateway
Develop a Proof of Concept and prototype
  Using .CZ Omnia Home Gateway & openWRT
  IoT device provisioning based on MUD
  Home Gateway App (Android/iPhone)
  Develop some IoT discoverable devices and MUD profiles
Use public GitHub to document the functional specification and repo for prototype software
  Functional specification (Work in progress)
  Open source software repository
  https://github.com/CIRALabs/Secure-IoT-Home-Gateway

## Slide 40: Specifications we are currently leveraging
Specifications we are leveraging:
https://datatracker.ietf.org/doc/draft-ietf-opsawg-mud/
https://datatracker.ietf.org/doc/draft-ietf-netmod-acl-model
RFC 7368
RFC 8375
https://datatracker.ietf.org/doc/draft-ietf-homenet-simple-naming
https://datatracker.ietf.org/doc/draft-ietf-homenet-front-end-naming-delegation
RFC 4033,4034,4035 (DNSSEC)
https://datatracker.ietf.org/doc/rfc5011/
RFC 4795
Specifications we are planning/considering:
RFC4301, RFC7296 (IPsec. Considering OpenVPN too)
RFC8366, https://datatracker.ietf.org/doc/draft-ietf-anima-bootstrapping-keyinfra/
https://datatracker.ietf.org/doc/draft-cheshire-dnssd-roadmap/
https://datatracker.ietf.org/doc/draft-ietf-dnssd-hybrid/
https://datatracker.ietf.org/doc/draft-cheshire-dnssd-roadmap/
https://datatracker.ietf.org/doc/draft-ietf-dnssd-mdns-relay/
Specifications we are writing:
draft-richardson-anima-smarkaklink-00
draft-richardson-opsawg-securehomegateway-mud-01
draft-richardson-shg-mud-quarantined-access-00
draft-richardson-shg-mud-quarantined-access-00