## Slide 1: SECURE HOME GATEWAY PROJECT
CIRA Labs
Secure Home Gateway Project
ICANN IDS Bangkok
Jacques Latour
May 10 & 11 2019
Notes: Consider starting with a story of your vision – how did this come to be?

## Slide 2: Project Evolution – From Idea in late 2016
Need security access controls
Developing a new framework to prevent lightbulbs from killing the internet!
Has to be easy to use
In the home
Gateway
x
x
?
MIRAI Dyn Attack
October 2016

## Slide 3: Secure Home Gateway (SHG) Goals
x
x
Protect the internet from IoT devices attacks
Protect IoT devices from internet attacks
x
Protect IoT
devices from internal attacks
Notes: The primary goal of this project is to develop a secure home gateway that;
  protects the internet from IoT devices attacks and
  protects home IoT devices from the internet attacks
  Protects IoT devices from internal attacks

## Slide 4: The many problems of today’s Home Gateway
No Standard Home Network Security Framework
No standard onboarding process
No outbound traffic security controls
Not globally reachable (no domain name)
No unique WIFI keys per home device
No device quarantining processes
No visibility on network activities
Home
Gateway

## Slide 5: IoT Device Security Landscape
Many are Vulnerable
Software is out of date
Focus: Time to market
Not to build correctly
Contribute to DDoS attacks
Cloud architecture dependencies
Compromise your network
Steal private information
Record video and voice
Steal WIFI credentials
Distribute malware
Send spam
Some are Unsupported
Many standards being developed
Full access to the ENTIRE Internet
Lack of secure testing and design
Require active monitoring

## Slide 6: IoT vendors are creating dependency on cloud architecture
At home
IoT Cloud
Services
On the road
Direct is better
Personal information is of great value to vendors
A domain name for the home makes this easier

## Slide 7: Project Evolution –> To a Secure Home Gateway (SHG) Prototype
MUD Server Repository / Curation
openWRT
Turris Omnia
CZNIC
SHG MUD Controller
Supervisor
SHG App “Ease of Use”
SIDN (.NL) SPIN
prpl Foundation
(prplWrt)
Mozilla IoT -
Web Thing API
SHG Security Access Controls
CIRA
DNS & SHG Provisioning
Standards Development
IETF, CSA/UL, ISO/IEC
Enhanced WIFI security
In progress:
DOTS, DNSSEC, Domain aware NFtable
Secure Home Gateway Framework
Running
Code
Proposed
Standards
Open
Source

## Slide 8: We put a team together to work on the idea
CIRA Labs
Sandelman Software
TwelveDot
Viagénie
TELUS
/ Algonquin College
SIDN Labs
Canadian Multistakeholder
Process: Enhancing IoT security
iotsecurity2018.ca
CIRA
Secure Home Gateway
Project

## Slide 9: Let’s look at the solution we have so far
Group Development
Forming
Storming
Norming
Performing
Mourning
Phase 1
PoC
Phase 2
Explore
Prototype
Phase 3
Agile Focus
Standards

## Slide 10: Criteria #1: “Has to be easy to use”
No passwords
Mobile Application
Swipe
Up Down Left Right
Scan & tap
Grandma

## Slide 11: Criteria #2: Apply enterprise security framework to home networks
Home Security
PDAP
Appliances
PDAP
Sensors
PDAP
Management
Application
IoT Cloud
Services
PDAP: Per Device Access Policy
Network Access Controls in the home network
Notes: -> best practices and new standards (note to Jacques – please explain Per Device Access Policy (PDAP) for those who may not understand what it means)
Rule #1: Identify IoT devices on your home network
Rule #2: Place a policy around the IoT device that restricts it to a specific function (default is no access)
Rule #3: Monitor for behavioural changes in the device and quarantine at the first sign of change.

## Slide 12: Challenge #1: A solution for Secure Home Gateway Initial Setup
SHG
application
https://datatracker.ietf.org/doc/draft-richardson-anima-smarkaklink/
BRSKI enrollment of with disconnected Registrars – smarkaklink
This document details the mechanism used for initial enrollment using a smartphone of a BRSKI Registrar system.
…where the registrar device is new out of the box and is the intended gateway to the Internet (such as a home gateway),
but has not yet been configured…
kaklink 
Standard
API
Notes: Follow the configuration instructions
  Install & open the CIRA SHG App
  Power on the SHG
  Scan the SHG QR code for initial setup
  System Assigned 3rd level domain name
  Setup split view Internet/External DNS for SHG domain
  Home Gateway ready for configuration

## Slide 13: Challenge #2: A solution for Home Network Device Onboarding
Grandma (the home admin) has to do something for each new devices
Unique WIFI keys per IoT device
By default new devices have <Deny All> policy until granted access
MUD to the rescue!
SGH
Full
Access
ACME Camera
Just connected
?
No
Access
IoT
Access
BEEP BEEP
You have a new device

## Slide 14: Challenge #3: A solution for IoT Device Quarantining
Who do we call?
The ISP help desk?
The IoT maker / vendor
The police?
The national CSIRT?
The home gateway vendor?
Need a standard for responding to IoT based cybersecurity events. WIP.
SGH
Monitor
ACME Fridge
Compromised
?
Release
Confirm Quarantine
BEEP BEEP
You have bad lettuce in the fridge

## Slide 15: New standard – MUD - Manufacturer Usage Description – RFC8520 – <YANG Modules>
I’m an ACME water sensor
- MUD File at: https://acme.corp/mud/ws1.0.json
MUD YANG Model:
- I have WIFI & apply the water sensor access policy
- I need to upgrade my firmware at https://acme.corp
- Configure me at https://myip/setup
- Alerts available at https://myip/alerts
It would be nice if the IoT device could advertise it’s current firmware version and/or current MUD file URL via WIFI or network connection (DPP, DHCP, LLDP…) in order to setup correct security profile

## Slide 16: IoT Device Onboarding Workflow
MUD Controller
(1)
Scan MUD
QR code &
send to MUD
Controller
(DHCP in future)
CIRA SHG
MUD Repository
SHG
App
(2)
Send to
CIRA
(2)
Get vendor
MUD file
ACME.CORP
MUD
Repository
SHG
ACME.CORP
IoT Water Sensor
(1)
(3)
User accepts
provisioning
instructions
MUD QR Code
(1)
(4)
IoT device added to network with specific network access controls
Network Access control:
Allow access to ACME.CORP
Allow to send alerts internally
Allow to be configured by app
Deny all other internet access
(4)
Netconf/Yang
(IP Tables)
MUD Supervisor
SPIN

## Slide 17: Recap: Secure Home Gateway (SHG)
MUD Server Repository / Curation
openWRT
Turris Omnia
CZNIC
SHG MUD Controller
Supervisor
SHG App “Ease of Use”
SIDN (.NL) SPIN
prpl Foundation
(prplWrt)
Mozilla IoT -
Web Thing API
SHG Security Access Controls
CIRA
DNS & SHG Provisioning
Standards Development
IETF, CSA/UL, ISO/IEC
Enhanced WIFI security
In progress:
DOTS, DNSSEC, Domain aware NFtable
Secure Home Gateway Framework
Running
Code
Proposed
Standards
Open
Source

## Slide 18
Questions?
https://cira.ca/cira-secure-home-gateway
https://github.com/CIRALabs
We are looking for sponsorship $$$ 